# ELECTRICAL FAN CONTROL OPERATION

• When the operation conditions are met for each function, the PCM sends an operation signal to cooling fan relay No.1 or No.2/No.3 to operate the cooling fan motors.

• The rotation speed of the cooling fan motor is switched between two levels according to a combination of the cooling fan relays.

• When only cooling fan relay No.1 is on, the rotation speed is low and when in addition to No.1, No.2 and No.3 are on, rotation speed is high.

| Function | Operation condition | Cooling fan motor | Cooling fan relay |
| --- | --- | --- | --- |
|  |  | No.1 | No.2 | No.1 | No.2/No.3 |
| Regular-driving cooling | ECT: Less than 97°C {206.6°F} | Stop | OFF | OFF |
|  | ECT: 97°C {206.6°F} or more | Low speed rotation | ON | OFF |
|  | • When all the following conditions are met: – ECT: 97°C {206.6°F} or more – During fuel cut at deceleration | Low speed rotation | ON | OFF |
|  | A/C amplifier (A/C switch): ON | Low speed rotation | ON | OFF |
|  | ECT: 101°C {213.8°F} or more | High speed rotation | ON |
|  | • When all the following conditions are met: – ECT: 101°C {213.8°F} or less – A/C amplifier (A/C switch): ON – Refrigerant pressure switch (medium-pressure switch): ON | High speed rotation | ON |
| After-cooling | • When all the following conditions are met: – Ignition switch: OFF – Drive-by-wire relay: OFF – Metering oil pump: Other than during ignition switch off mode – Engine compartment temperature high. | High speed rotation | ON |
|  | • When all the following conditions are met: – Ignition switch: OFF – Drive-by-wire relay: OFF – Metering oil pump: Other than during ignition switch off mode – ECT: 110°C {230°F} or more | High speed rotation | ON |
| Forced drive | During test mode (during test mode with WDS) when the AP is depressed. | High speed rotation | ON |
| Fail safe | When a failure occurs in the ECT sensor. | High speed rotation | ON |