| PID | Description |
| --- | --- |
| 0x00 | Supported PIDs 0x01 to 0x1F |
| 0x01 | Number of trouble codes, MIL indicator on/off, and available onboard tests |
| 0x02 | Freeze frame DTC |
| 0x03 | Fuel system status |
| 0x04 | Calculated engine load value |
| 0x05 | Engine coolant temperature |
| 0x06 | Short term fuel % trim - Bank 1 |
| 0x07 | Long term fuel % trim - Bank 1 |
| 0x08 | Short term fuel % trim - Bank 2 |
| 0x09 | Long term fuel % trim - Bank 2 |
| 0x0A | Fuel pressure |
| 0x0B | Intake manifold pressure |
| 0x0C | Engine RPM |
| 0x0D | Vehicle speed |
| 0x0E | Timing advance |
| 0x0F | Intake air temperature |
| 0x10 | Mass air flow rate |
| 0x11 | Throttle position |
| 0x12 | Secondary air status |
| 0x13 | Oxygen sensors present |
| 0x14 | Oxygen sensor voltage, Short term fuel trim (Bank 1, Sensor 1) |
| 0x15 | Oxygen sensor voltage, Short term fuel trim (Bank 1, Sensor 2) |
| 0x16 | Oxygen sensor voltage, Short term fuel trim (Bank 1, Sensor 3) |
| 0x17 | Oxygen sensor voltage, Short term fuel trim (Bank 1, Sensor 4) |
| 0x18 | Oxygen sensor voltage, Short term fuel trim (Bank 2, Sensor 1) |
| 0x19 | Oxygen sensor voltage, Short term fuel trim (Bank 2, Sensor 2) |
| 0x1A | Oxygen sensor voltage, Short term fuel trim (Bank 2, Sensor 3) |
| 0x1B | Oxygen sensor voltage, Short term fuel trim (Bank 2, Sensor 4) |
| 0x1C | OBD standards this vehicle conforms to |
| 0x1D | Oxygen sensors present 2 |
| 0x1E | Auxiliary input status |
| 0x1F | Run time since engine start |
| 0x20 | Supported PIDs 0x21 to 0x3F |
| 0x21 | Distance traveled with malfunction indicator lamp (MIL) on |
| 0x22 | Fuel rail pressure (relative to manifold vacuum) |
| 0x23 | Fuel rail pressure (diesel) |
| 0x24 | Oxygen sensor 1 equivalence ratio (lambda value) |
| 0x25 | Oxygen sensor 2 equivalence ratio (lambda value) |
| 0x26 | Oxygen sensor 3 equivalence ratio (lambda value) |
| 0x27 | Oxygen sensor 4 equivalence ratio (lambda value) |
| 0x28 | Oxygen sensor 5 equivalence ratio (lambda value) |
| 0x29 | Oxygen sensor 6 equivalence ratio (lambda value) |
| 0x2A | Oxygen sensor 7 equivalence ratio (lambda value) |
| 0x2B | Oxygen sensor 8 equivalence ratio (lambda value) |
| 0x2C | Commanded EGR |
| 0x2D | EGR error |
| 0x2E | Commanded evaporative purge |
| 0x2F | Fuel level input |
| 0x30 | Number of warm-ups since codes cleared |
| 0x31 | Distance traveled since codes cleared |
| 0x32 | Evap system vapor pressure |
| 0x33 | Barometric pressure |
| 0x34 | Oxygen sensor 1 equivalence ratio (lambda value) |
| 0x35 | Oxygen sensor 2 equivalence ratio (lambda value) |
| 0x36 | Oxygen sensor 3 equivalence ratio (lambda value) |
| 0x37 | Oxygen sensor 4 equivalence ratio (lambda value) |
| 0x38 | Oxygen sensor 5 equivalence ratio (lambda value) |
| 0x39 | Oxygen sensor 6 equivalence ratio (lambda value) |
| 0x3A | Oxygen sensor 7 equivalence ratio (lambda value) |
| 0x3B | Oxygen sensor 8 equivalence ratio (lambda value) |
| 0x3C | Catalyst temperature (Bank 1 Sensor 1) |
| 0x3D | Catalyst temperature (Bank 2 Sensor 1) |
| 0x3E | Catalyst temperature (Bank 1 Sensor 2) |
| 0x3F | Catalyst temperature (Bank 2 Sensor 2) |
| 0x40 | Supported PIDs 0x41 to 0x5F |
| 0x41 | Monitor status this drive cycle |
| 0x42 | Control module voltage |
| 0x43 | Absolute load value |
| 0x44 | Command equivalence ratio |
| 0x45 | Relative throttle position |
| 0x46 | Ambient air temperature |
| 0x47 | Absolute throttle position B |
| 0x48 | Absolute throttle position C |
| 0x49 | Accelerator pedal position D |
| 0x4A | Accelerator pedal position E |
| 0x4B | Accelerator pedal position F |
| 0x4C | Commanded throttle actuator |
| 0x4D | Time run with MIL on |
| 0x4E | Time since trouble codes cleared |
| 0x4F | External test configuration #1 |
| 0x50 | External test configuration #2 |
| 0x51 | Fuel type |
| 0x52 | Percentage of alcohol fuel mix |
| 0x53 | Absolute evap system vapor pressure |
| 0x54 | Evap system vapor pressure |
| 0x55 | Short term secondary oxygen sensor trim bank 1 and bank 3 |
| 0x56 | Long term secondary oxygen sensor trim bank 1 and bank 3 |
| 0x57 | Short term secondary oxygen sensor trim bank 2 and bank 4 |
| 0x58 | Long term secondary oxygen sensor trim bank 2 and bank 4 |
| 0x59 | Fuel rail pressure (absolute) |
| 0x5A | Relative accelerator pedal position |
| 0x5B | Hybrid battery pack remaining life |
| 0x5C | Engine oil temperature |
| 0x5D | Fuel injection timing |
| 0x5E | Fuel rate |
| 0x5F | Emission requirements for this vehicle |